Defining the 3995 Series C  Optical Jukebox to ADSM

From the AIX command line on MLWARS02 enter the following

smitty

Devices

Read/Write Optical Drive

List All Defined R/W Optical Drives

- The following information will be listed.  Note the SCSI address

00-14-01-0; this will be needed later.

omd0 Available 00-14-01-0,0 SCSI Read/Write Optical Drive

omd1 Available 00-14-01-1,0 SCSI Read/Write Optical Drive

omd2 Available 00-14-01-2,0 SCSI Read/Write Optical Drive

omd3 Available 00-14-01-3,0 SCSI Read/Write Optical Drive

omd4 Available 00-14-01-4,0 SCSI Read/Write Optical Drive

omd5 Available 00-14-01-5,0 SCSI Read/Write Optical Drive

exit smitty

enter smitty

Devices

ADSM Devices

Optical R/W Disk Drive

Add a Optical Disk Drive

- the following information will be displayed.  Select it.

ADSM-SCSI-OP scsi ADSM Read/Write Optical Drive

* the following information will be displayed

x   vscsi0 Available 00-08-00 SCSI I/O Controller Protocol Device          x

x   vscsi1 Available 00-08-01 SCSI I/O Controller Protocol Device          x

x   vscsi2 Available 00-14-00 SCSI I/O Controller Protocol Device          x

x   vscsi3 Available 00-14-01 SCSI I/O Controller Protocol Device          x

x   vscsi4 Available 00-15-00 SCSI I/O Controller Protocol Device          x

- select the statement that correlates with the SCSI address obtained      earlier.  In this case 14-01

The following screen will appear

[Entry Fields]

Optical Disk Drive Type                             ADSM-SCSI-OP

Optical Disk Drive Interface                        scsi

Description                                         ADSM Read/Write Optica>

Parent adapter                                      vscsi3

* CONNECTION address                                 []                       +

For connection address insert 0,0 press enter.  This will need to be repeated for 1,0 2,0 3,0 4,0 and 5,0

From the ADSM DEVICES screen  (smitty, devices, ADSM devices) select

Library/MediumChanger

Add a Library/MediumChanger

- the follwoign information will be displayed.

- Select the lb0 statement

ibmjb0 Available 00-14-01-6,0 IBM 3995-C68 Optical Disk Library

lb0    Available 00-14-01-6,0 ADSM Library

The following screen will be displayed.  Enter 6,0  for the connection address

[Entry Fields]

Library/MediumChanger Type                          ADSM-SCSI-LB

Library/MediumChanger interface                     scsi

Description                                         ADSM Library

Parent adapter                                      vscsi3

* CONNECTION address                                 []                       +

Run cfgmfr from the AIX command line.  The optical library should be up and online.